## Slide 1: Web of Trust for Android Applications
By James Kasten

## Slide 2: Organization
Motivation and Proposed Solution
  Common Reputation System Errors
  Design Principles and Considerations
Specific Design Specifications
Detection of Malicious Behavior
Simulations
  Setup and Assumptions
  Results
Further Implementation
Future Work

## Slide 3: Motivation
Google Android Market is very open
Android Security and Privacy permissions are controlled by the user
User has little information regarding use of permissions

## Slide 4: Some Existing Solutions
TaintDroid
  Tracks the flow of private information through the phone
  Notifies the user when private information is sent across the network
  Requires advanced and knowledgeable users to operate
Kirin
  Based purely on installation privileges
  Only as effective as the user makes it

## Slide 5: Proposed Solution
Provide a mechanism that allows privacy and security information of third-party applications to flow from advanced users to novices
Web of Trust enhanced with Automated Analysis
  Web of Trust Examples: Epinions.com, MyWOT.com (internet sites), Google PageRank

## Slide 6: Common Reputation System Problems
Lack of ability to differentiate dishonest feedback from honest ones
Most systems provide no support against users gaming the system
No incentives for feedback
Sybil Attack

## Slide 7: Web of Trust Key Features
Large disparity of knowledge in user base
  Special two-tiered reputation system
Global Trust Index
Centralized Server
  Algorithms need to be computationally inexpensive
Additional information provided to the user with some automated analysis

## Slide 8: Web of Trust Components
User Rating System
  Review Types
    Application Ratings
    Rating Reviews
  Additional Influences
    User Reputation
    Application Author Rating
Automated Analysis
  Assess static privileges
  Analyze TaintDroid logs for each application
  Create/Analyze power consumption profiles

## Slide 9: User Rating System
Tetroid by SoftwareWorks Trust Index 7.8
Tetroid by SoftwareWorks Trust Index 7.7
Application Ratings
  Influence determined by user’s reputation
  Effects both Application Trust Index and Author’s Trust Index
Review Ratings
  Either positive or negative
  Affects user reputation
  Influence determined by reviewer’s user reputation
James’s Rating 7
According to TaintDroid, this app occasionally sends out your location to WebAdds.com. Other than that, it appears safe.

## Slide 10: User Rating System
Provide Global Trust Index for each application
Calculating the Trust Index
2/3 Global Application Rating + 1/3 Author Rating
Calculating Global Application Rating
∑ (AppRating.user.reputation * AppRating.PrivacyRating) / Accuracy
Accuracy = ∑ (AppRating.user.reputation)
Calculating Author’s Rating
  ∑ (Application.Accuracy * Application.TrustIndex) / (∑ Application.Accuracy)

## Slide 11: Reputation
New users assigned reputation of .5
Cap user reputation between [0, 10]
Reputation Calculation for User
  Stops user from gaining max reputation from a single rating
Formulated to separate novice users from experienced users
For each (ApplicationRating) {
appRatingRep = ∑ ((ReviewRating.user.reputation / 10) * Rating)
if ( appRatingRep > 1)
discount additional reputation by factor of 5
add appRatingRep to reputation
}

## Slide 12: Propagation of New Information
Review Rating is submitted - O(1)
Local user reputation is updated - O(1)
Reputation change is propagated to those users immediately affected – O(n)
for each (AppRating in users List), add it to set of dirtyApplications - O(n)
After period of time, recalculate all dirtyApplication AppRatings and Author Ratings O(nm)
Calculate new Trust Index - O(1)

## Slide 13: Reputation Guards
Maximum of 5 review ratings (thumbs up/ thumbs down) per application
  Stops user from trashing or boosting an applications trust index indirectly
Recent Activity Window - Small weighted trust rating maintained and used to punish users with recent low performance
  Guards against users using high rep to game the rankings

## Slide 14: Reputation Guards - Recent Activity Window
Look at the last past 3 application ratings of users with high reputation
If weighted average of Review Ratings is less than threshold, punish user
Weighted average of review ratings
  Recent Performance
∑ AppRating.ReviewRating * AppRating.ReviewRating.user.reputation
∑ AppRating.ReviewRating.user.reputation

## Slide 15: Determining Punishment
Recent performance domain [-1, 1]
Current performance threshold is -.1
Reputation Punishment
  rep = rep / (1 + ((-performance) * (accuracy / WEIGHT_FACTOR)))
    Current weight factor is 5

## Slide 16: Simulation
Experienced Users
  Rate accurately with standard deviation of 1
Average Users
  Rate only half of the applications
  Rate apps fairly accurately with st dev of 3
Ignorant Users
  Rate randomly on a uniform distribution
Malicious Users
  Act like experienced users, but when their reputation is high they game the system

## Slide 17: Additional Assumptions
Ignorant and Average users are expected to recognize experienced user and malicious user application reviews at a rate of .8
  Users recognize the experienced vocabulary and rate it up
Experienced users are not as easily fooled by malicious users and only rate up an App Rating if the trust value is relatively “close” to their own opinion (± 1)

## Slide 18: Normal User Application Ratings
Normal user application ratings are rated up if the corresponding reviewer has a similar opinion
  Rated up if rating is within ± 1 of their opinion
Rated down if the reviewer’s opinion is differs from App Ratings author by more than ± 1

## Slide 19: Simulation Results
Chart: Ignorant Users
| 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45 | 48 | 51 | 54 | 57 | 60
Error | 0.38585 | 0.37826 | 0.3665 | 0.38295 | 0.37206 | 0.37517 | 0.36261 | 0.36407 | 0.44221 | 0.39187 | 0.40197 | 0.44726 | 0.65541 | 0.6682 | 0.60233 | 0.78029 | 0.88742 | 1.0525 | 1.1954 | 1.2125 | 1.86
EXP | 10 | 10 | 9.9515 | 9.9309 | 9.8962 | 9.3343 | 9.1357 | 7.877 | 7.0122 | 7.2582 | 5.581 | 4.2347 | 4.0538 | 3.7025 | 2.8421 | 2.9266 | 2.3417 | 1.9641 | 1.9721 | 1.3881 | 0.33506
AVG | 0.93517 | 0.85907 | 0.75711 | 1.0836 | 0.87488 | 0.84604 | 0.76883 | 0.56541 | 0.6841 | 0.71494 | 0.61582 | 0.47922 | 0.59195 | 0.62064 | 0.54429 | 0.70245 | 0.65419 | 0.69714 | 0.68283 | 0.79136 | 1.1773
IGN | 0 | 0 | 0.043925 | 0.031369 | 0 | 0.0051122 | 0.0056453 | 0.04786 | 0.044821 | 0.018926 | 0.050748 | 0.041036 | 0.16775 | 0.23501 | 0.078176 | 0.30237 | 0.30565 | 0.3492 | 0.45622 | 0.45375 | 1.1849
Apps = 20
Exp Users = 5
Avg Users = 30
Mal Users = 0

## Slide 20: Simulation with Malicious Users
Chart: Malicious Users
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Error | 0.40964 | 0.42839 | 0.45946 | 0.45497 | 0.50253 | 0.43497 | 0.44323 | 0.47962 | 0.44808 | 0.48395 | 0.56372 | 0.56101 | 0.58226 | 0.57349 | 0.53647 | 0.49808 | 0.67348 | 0.60335 | 0.66125 | 0.66879 | 0.65492
EXP | 6.1802 | 5.7235 | 8.4747 | 8.5704 | 9.4295 | 9.1033 | 9.3682 | 9.7318 | 9.4969 | 9.4754 | 9.7971 | 9.9971 | 9.8652 | 9.986 | 10 | 9.9499 | 9.8853 | 9.9181 | 9.9732 | 9.9852 | 9.7427
AVG | 0.70138 | 0.61468 | 0.86248 | 0.82078 | 0.93832 | 0.70124 | 0.76102 | 0.87366 | 0.68279 | 0.70963 | 0.8769 | 0.80734 | 0.73509 | 0.75706 | 0.78491 | 0.69069 | 0.87099 | 0.66517 | 0.75729 | 0.76902 | 0.83052
IGN | 0.056757 | 0.069818 | 0.055019 | 0.033186 | 0.030361 | 0.040477 | 0.043479 | 0.044859 | 0.023718 | 0.042967 | 0.058011 | 0.037205 | 0.047036 | 0.046846 | 0.032449 | 0.018093 | 0.01659 | 0.018953 | 0.034686 | 0.0075092 | 0
MAL | 0 | 3.4272 | 4.4515 | 4.9671 | 4.278 | 4.4163 | 3.7437 | 4.2747 | 4.1107 | 3.8977 | 4.2738 | 4.1677 | 3.8384 | 3.8774 | 4.1099 | 3.5304 | 4.2507 | 3.9578 | 3.9542 | 4.2018 | 3.6689
Apps = 20
Exp Users = 5
Avg Users = 30
Ign Users = 30

## Slide 21: Simulation Time Duration
Chart: Number of Rated Applications
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Error | 0.86135 | 0.92182 | 0.83937 | 0.53946 | 0.53729 | 0.44228 | 0.40588 | 0.4201 | 0.36937 | 0.34887 | 0.36946 | 0.35573 | 0.33497 | 0.32548 | 0.35408 | 0.35839 | 0.40562 | 0.41602 | 0.40458 | 0.39153 | 0.52359 | 0.37568 | 0.37465 | 0.42901 | 0.46583 | 0.47572 | 0.47857 | 0.48658 | 0.49177 | 0.47498
EXP | 0.69196 | 0.92353 | 1.1715 | 1.3482 | 1.6423 | 1.8177 | 2.2557 | 2.5379 | 2.8655 | 3.1712 | 4.0311 | 4.2257 | 5.9933 | 6.3033 | 6.8532 | 6.5797 | 8.4014 | 8.7093 | 8.6091 | 9.2225 | 9.7693 | 9.0643 | 9.4177 | 9.3673 | 9.6085 | 9.761 | 9.7982 | 9.5089 | 9.5397 | 9.7106
AVG | 0.45525 | 0.45235 | 0.43119 | 0.43438 | 0.42674 | 0.44605 | 0.49149 | 0.44219 | 0.46522 | 0.44324 | 0.56737 | 0.52384 | 0.72192 | 0.63061 | 0.64972 | 0.54967 | 0.65392 | 0.69885 | 0.64158 | 0.53956 | 0.77009 | 0.67815 | 0.55645 | 0.72957 | 0.73057 | 0.55238 | 0.53801 | 0.64405 | 0.54999 | 0.59509
IGN | 0.36268 | 0.24119 | 0.19155 | 0.13818 | 0.12817 | 0.12277 | 0.075599 | 0.097852 | 0.076345 | 0.051557 | 0.089119 | 0.04185 | 0.034606 | 0.049293 | 0.063287 | 0.040133 | 0.035729 | 0.031922 | 0.03862 | 0.036842 | 0.016112 | 0.017881 | 0.021214 | 0.014931 | 0.003248 | 0.00049087 | 0.015285 | 0 | 0.010543 | 0.0078009
MAL | 0.66597 | 0.87739 | 1.0229 | 1.1114 | 1.4319 | 1.5657 | 1.8568 | 1.6566 | 2.2859 | 2.2197 | 3.2444 | 3.0926 | 3.8201 | 3.8233 | 4.4125 | 3.7228 | 4.0244 | 4.0267 | 4.132 | 3.6923 | 3.764 | 3.2691 | 3.3865 | 3.4596 | 3.1547 | 2.9884 | 2.7975 | 2.994 | 2.6728 | 3.3913
Exp Users = 5
Avg Users = 30
Ign Users = 30
Mal Users = 5

## Slide 22: Automated Analysis
Access Application Manifest file to assess static privileges
Classify Application Privacy and Security as Safe, Some Risk, Potentially Dangerous
  Safe – No access to private information, accounts and money
  Some Privacy Risk – Access to both private information and internet access
  Potentially Dangerous – Access to accounts and money

## Slide 23: Implementation
Google App Engine
  Works well with Android Applications
Android Application
  Users based on Google Accounts and phone numbers
    Android Market requires user to have valid account
    Should effectively avoid Sybil attack
  Quick Example

## Slide 24: Advantages
Self-sustaining
Computationally light
Makes the market more efficient as users have increased knowledge of the applications
Accuracy increases as users are able to gather more information

## Slide 25: Disadvantages
Requires critical mass to provide reliable ratings
Ensuring authenticity of automated information and developing an appropriate metric is difficult
Need to implement a light clustering algorithm to provide protection against a distributed attack

## Slide 26: Future Work – User Rating System
Potential bias for negative ratings
  Establish baseline for expected negative ratings per download
  Adjust Trust Index based on downloads and ratings
Implement lightweight clustering technique to identify groups of malicious users
  Potential – Root Mean Square algorithm to determine level of similarity between users
Implement Yahoo Answers like point system

## Slide 27: Future Work - Automated Analysis
Look into providing static analysis of static privileges through Kirin system
Implement / incorporate rest of the automated analysis

## Slide 28: Main References
[1] TaintDroid: An Information-Flow Tracking System for Realtime Privacy Monitoring on Smartphones, William Enck, Peter Gilbert, Byung-gon Chun, Landon P. Cox, Jaeyeon Jung, Patrick McDaniel, and Anmol N. Sheth, OSDI, October 2010.
[2] R. Guha. Open rating systems. Technical report, Stanford University, 2003.
[3]Leveraging Robust Service Evaluation by Introducing the Web of Trust, Cai, Sibo, Yanzhen Zou, Bing Xie, and Weizhong Shao, CLOUD '09 190-97.
[4]Kui Meng; Yue Wang; Xu Zhang; Xiao-chun Xiao; Geng-du Zhang; , "Control Theory Based Rating Recommendation for Reputation Systems," Networking, Sensing and Control, 2006. ICNSC '06. Proceedings of the 2006 IEEE International Conference on , vol., no., pp.162-167,
[5]Rein, G.L.; , "Reputation Information Systems: A Reference Model," System Sciences, 2005. HICSS '05. Proceedings of the 38th Annual Hawaii International Conference on , vol., no., pp. 26a- 26a, 03-06 Jan. 2005
[6]L. Xiong and L. Liu. “PeerTrust: Supporting Reputation-Based Trust for Peer-to-Peer Electronic Communities”, in IEEE Transactions on Knowledge and Data Engineering, 16(7), 2004, pp. 843-857.
[7]W. Enck, M. Ongtang, and P. McDaniel, “On Lightweight Mobile Phone Application Certification,” in Proceedings of ACM CCS, November 2009.
[8]A. Cheng and E. Friedman, “Sybilproof reputation mechanisms,” in Proc. ACM SIGCOMM P2PECON workshop, pp. 128–132, 2005.